## Slide 1: Antennas and Feedlines
Sections

## Slide 2: ?Antenna Gain?
dbi or dbd ?

## Slide 3: ?Antenna Gain?
Gain of a dipole is 2.15 db greater
than an isotropic. G9C04
Main lobe, direction of maximum radiated field strength G9C08
F/B
G9C07

## Slide 4: Vertical antenna pattern
G9B03
Omni-Directional

## Slide 5: Dipoles
Horizontal dipole feed point impedance ≅ 72 ohms
¼ wavelength
½ wavelength
E
Maximum radiation (fig. 8) at right angles to antenna G9B04
300
Frequency
(MHz)
Wavelength
Meters

## Slide 6: Dipoles
Horizontal dipole feed point impedance ≅ 72 ohms
½ wavelength
What is the approximate length in feet of a 1/2 wave dipole for 14.25 MHz.
Calculate using metric
measurements
8 ft
16 ft
24 ft
32 ft
G9B10
300
Frequency
(MHz)
Wavelength
Meters
468 / Freq(MHz)
468 / Freq(MHz)
or
20 mtr
= 32.8 ft.

## Slide 7: Dipoles
½ wavelength
What is the approximate length in feet of a 1/2 wave dipole for 3.55 MHz.
Calculate using metric
measurements
42 ft
84 ft
131 ft
263 ft
G9B11
300
Frequency
(MHz)
Wavelength
Meters
468 / Freq(MHz)
468 / Freq(MHz)
or
= 131.8. ft.
80 mtr

## Slide 8: Dipoles
½ wavelength
Impedance increases as feed point is moved away from center G9B08
Impedance = E/I
E
Increase Z
Feed point impedance of a half wave end fed would be very high. G9D02

## Slide 9: Vertical Antennas with Ground Planes
¼ wavelength
Ground plane
¼ wavelength radius min.
Feed point ≅ 35 ohms
Radials can be laying on the ground or buried G9B06
¼ wavelength
¼ wavelength
Feed point ≅ 35 ohms

## Slide 10: Vertical antenna impedance
°
°
°
≅35 Ω
≅50 Ω
≅72 Ω
G9B02
How can we change the feed point impedance of a quarter wave ground plane antenna
What happens to the feed-point impedance of a ground-plane antenna when its radials are changed from horizontal to downward-sloping?
It increases

## Slide 11: Vertical Antenna Length Calculation
Use Metric measurements for calculations
G9B12
What is the approximate length in feet for a 1/4-wave vertical antenna cut for 28.5 MHz?
A. 8 feet
B. 11 feet
C. 16 feet
D. 21 feet
(A)
234 / Freq (MHz)
or
234 / Freq (MHz)
10 mtr
= 8.21. ft.

## Slide 12: Mobile HF Antennas
Capacitive hat, electrically lengthens the antenna G4E01
Loading coil
"corona ball” G4E02
Operating on a short mobile antenna reduces operating bandwidth G4E06

## Slide 13: Random Wire Antenna
Feed point is random impedance
Antenna tuner must be used
May result with high RF currents and voltages on equipment and in the shack.
These could result in RF burns. G9B01

## Slide 14: How High?
½ wavelength
A change in antenna height above the ground, changes the feed point impedance in a dipole.
Below ½ wavelength in height, as antenna gets closer to the ground the feed point impedance decreases. G9B07
Below ½ wavelength in height, as antenna gets closer to the ground the azimuth pattern becomes more Omni directional. G9B05

## Slide 15: Horizontal Advantage
Horizontal polarized antennas have Lower ground reflection losses G9B09

## Slide 16: Yagi
Reduced interference from the sides and behind
Direction of gain
Reflector
(parasitic)
Director
(parasitic)
Driven element
½ wave dipole
G9C02
Shorter than
driven element
G9C03
Longer than
driven element
G9C03
Front to Back Ratio
The power radiated in the major direction, compared to the power in opposite direction. G9C07
Theoretical max forward gain
of a three element Yagi 9.7 dBi
G9C11

## Slide 17: Yagi
Increase the diameter of the elements you increase band width G9C01
A longer boom and adding directors, increases gain. G9C05
More directors increase gain
When designing a Yagi, all of the following variables need to be considered. G9C10
A. The physical length of the boom
B. The number of elements on the boom
C. The spacing of each element along the boom
14.000
14.350
Feed point impedance of a Yagi
20 to 25 ohms typical
Red lines Represent bandwidth

## Slide 18: Gamma, thanks to the Greek

## Slide 19: Impedance Matching
In a Yagi antenna, a gamma mach is used to To match the relatively low feed-point impedance to 50 ohms
An advantage of a gamma match, The driven element does not need to be insulated from the boom. G9C12
Several other types of matching methods are used,
And can be found in the ARRL antenna handbook

## Slide 21: The hairpin match
A shorted transmission line stub placed at the feed point of a Yagi antenna to provide impedance matching. G9C16

## Slide 23: Loop Antenna
A loop antenna consists of a long usually 1 wavelength or longer looped conductor, with the feed point at the two ends.
Shortened loop antennas will have nulls broadside to the plane. G9D10
Virtually omnidirectional with a lower peak vertical radiation angle than a dipole. G9D13

## Slide 24: Quad Antenna
Feed point at the bottom of the loop,
Horizontal polarization.
Feed point at the side of the loop,
Vertical polarization polarization.
Reflector element approximately 5 % longer. G9C06
Length of each side is approx. ¼ wavelength. G9C13

## Slide 25: ‘bout the same
G9C14
How does the forward gain of a two-element quad antenna compare to the forward gain of a three-element Yagi antenna?
A. About 2/3 as much
B. About the same
C. About 1.5 times as much
D. About twice as much
How does the gain of a two-element delta-loop beam compare to the gain of a two-element quad antenna?
A. 3 dB higher
B. 3 dB lower
C. 2.54 dB higher
D. About the same
(B)
(D)

## Slide 26: Halo Antenna
Omni-directional in the plane of the halo. G9D03

## Slide 27
Screwdriver mobile antenna
A “screwdriver” mobile antenna adjust its feed-point impedance by varying the base loading inductance. G9D08

## Slide 28: NVIS Near Vertical Incidence Sky-wave
G9D01
http://www.athensarc.org/nvis.asp
Antenna heights between .1λ to .25 λ
NVIS Advantage:
High vertical angle radiation for working stations within a radius of a few hundred kilometers
Short distance MF or HF propagation using high elevation angles G3C10

## Slide 29: Stacked Antennas
Vertically stacking antennas increase the gain and narrows the elevation beam width G9D05
Stacking two horizontal Yagis at ½ λ apart increases gain 3dB
G9C09

## Slide 30: Log Periodic Antenna LPA
LPA Advantage
Wide band width. G9D06
Length and spacing of the elements increases logarithmically from one end of the boom to other. G9D07

## Slide 31: Beverage Antenna Traveling Wave Antenna
A long low directional receiving antenna
Usually less than 20 ft. in height
Receiving end terminated with a resistor
The beverage antenna has high losses, not suitable for transmitting
The primary use for the Beverage antenna is for receiving on the low HF bands G9D09
Invented by Harold Beverage in 1922

## Slide 32: Beverage Antenna

## Slide 33: Multi Band Antennas
Traps are used to permit multiband operation. G9D04
Disadvantage of trap antennas,
Trapped antennas have poor harmonic rejection. G9D11
Traps have losses and reduce the efficiency of the antennas.

## Slide 34: Feed Lines
All Feed lines have a characteristic impedance
The impedance is based on the following physical characteristics:
The geometry of the feed line conductors
The distance between the the center of the conductors
The radius of the conductors. G9A01
Flat line twin conductor window feed line = 450 ohms G9A03
For amateur radio use, we use coax feed line with 50 and 75 ohm impedance. G9A02
All feed lines have loss. Usually measured in dB loss/ 100 Ft. G9A06
As frequency increases, loss increases G9A05
Small diameter feed lines generally have higher losses than large diameter.

## Slide 35: Coax Loss

## Slide 36: SWR
Reflected power can occur when ever there is a mismatch in impedance G9A04
Standing waves occur whenever reflected waves interfere with forward waves.
SWR is always greater than 1:1
G9A09
What standing wave ratio will result from the connection of a 50-ohm feed line to a non-reactive load having a 200-ohm impedance?
A. 4:1
B. 1:4
C. 2:1
D. 1:2
G9A10
What standing wave ratio will result from the connection of a 50-ohm feed line to a non-reactive load having a 10-ohm impedance?
A. 2:1
B. 50:1
C. 1:5
D. 5:1
SWR is the ratio of the higher impedance to the lower. SWR = higher impedance/lower
(A)
(D)
There are five similar questions G9A09 – G9A13

## Slide 37: SWR vs. Loss

## Slide 38: Impedance Matching
The ideal situation is to have feed line and load impedance match
to prevent standing waves G9A07
Most often the impedance is matched between the transmitter and the feed line.
This matching is usually done with an antenna coupler or antenna tuner G4A06

## Slide 39
Transmitter
50 Ω impedance
Antenna
50 Ω impedance
Feed line 50 Ω
SWR = 1:1
G9A11
What standing wave ratio will result when connecting a 50 ohm feed line to a non-reactive load having 50 ohm impedance?

## Slide 40
Transmitter
50 Ω impedance
Antenna
200 Ω impedance
Feed line 50 Ω
SWR = 4:1
G9A09
36% loss of power
What standing wave ratio will result when connecting a 50 ohm feed line to a non-reactive load having 200 ohm impedance?

## Slide 41
Transmitter
50 Ω impedance
Antenna
250 Ω impedance
Feed line 50 Ω
SWR = 5:1
G9A08
Antenna Tuner
G4A06
If the SWR on an antenna feed line is 5 to 1, and a matching network at the transmitter end of the feed line is adjusted to 1 to 1 SWR, what is the resulting SWR on the feed line?

## Slide 42: How do we measure impedance matching and SWR
Antenna Analyzer
SWR Meter
G4B10

## Slide 43: For Next Week
Study flash cards www.hamexam.org
73
Tom and Jack
Lesson 1
G1A
G1C
G2A
G2B
G2C
G2D
G4A part
G4D part
Lesson 6
G4E
G9A
G9B
G9C
G9D
Lesson 8/9
G4A
G4B
G4C
G4D
G7B
G7C
G8A
G8B
Lesson 4
G5A
G5B
G6A
G6B
Lesson 11
G0A
G0B
Radio
Fundamentals
ARRL Ch. 1, 2, 3, 6
Antennas
ARRL Ch. 7
Equipment
ARRL Ch. 5
Electricity
ARRL Ch. 4
Safety
Ch. 9
Lesson 2
G1B
G1D
G2A
G2E
G8C
Lesson 3
G5B
G5C
Resistors
Capacitors
AC Power
The Reactive
components
Lesson 5
G4B
G4E
G6A
G6B
G7A
G7B
Semi-
conductors
Propagation
ARRL Ch. 8
Lesson 7
G3A
G3B
G3C
Digital
ARRL Ch. 6
Lesson 10
G1E
G2E
G8A
G8B
G8C