## Slide 1: Digital Modes

## Slide 2: Digital Modes
1. Protocol
2. Method of modulation
The directions for the particular mode.
How the information is coded
FM
SSB
AFSK
PSK
Digital modes are restricted to the CW/DATA sub band.

## Slide 3: Where do we find digital modes in the bands
CW and Data portions of the bands
On 20 meters digital is found at 14.070 to 14.1 MHz
On 80 meters found at 3570 to 3600 kHz
Phone and image
RTTY, Data. And CW
E
14.025
14.150
14.175
A
G
14.225
14.000
14.350
14.070
14.112
PSK31
G2E07
G2E04
G2E08 PSK31 found below RTTY

## Slide 4: RTTY “Teletype” Narrowband direct printing telegraphy
Originated in 1930
Protocol
Uses the Baudot Code
Five bits + start and stop
G2E06 Shift between mark and space = 170 Hz
On HF 45 bauds or 60 WPM most common
Modulation
AFSK
Via LSB G2E01
Popular in all HF bands
G8C04
Cannot decode an RTTY or other FSK signal even though it is apparently tuned in properly?
A. The mark and space frequencies may be reversed
B. You may have selected the wrong baud rate
C. You may be listening on the wrong sideband
AOTA

## Slide 5: PACTOR Packet Teletype Over Radio
Improvement over RTTY with the ability to detect and correct errors.
Three versions: PACTOR I, PACTOR II PACTOR III
Modulation
FSK and PSK used in PACTOR III
Most common on HF for exchanging large amounts of information.
Used in Winlink email. www.winlink.com. G2E13
NAK response from receive station = Requesting re-transmission
Operation
Any signals or modes can interfere with PACTOR or WINOR G2E03. AOTA
Re-Tries……Timeouts…….Pauses…….Failure to connect. G2E03
Limited between two stations only
Can not join ongoing conversation
G2E09
G8C05
Limited between two stations only
Can not join ongoing conversation
Monitor without connect to check for busy G2E02
Bandwidth 2300 Hz. G8B05
Notes: NAK= Not Acknowledged

## Slide 6: PSK31 Phase Shift Keying 31 baud
Protocol
Uses a variable length code 5, 7, or 8 bits
Shorter code for common characters
Upper case letters use longer Varicode. G8C08
Called Varicode G8C12
Modulation
Phase Shift Keying
Via SSB
Very common on HF
Keyboard to Keyboard
Advantage
Uses very narrow bandwidth
Uses computer soundcard
G8C09

## Slide 7: Packet Radio
Protocol
AX.25 protocol standard.
7 bit code + start, stop, and parity bit.
Modulation
FSK,
Operation
Transmitted in a group of characters (packets)
Each starts with a header. G8C03
provides information about the routing and handling.
Most common on VHF and VHF
G8C07 ERRORS Receive station responds with ARQ = Send packet again

## Slide 8: FT8
Digital mode designed for signals with very low signal to noise ratio. G8A12
8 tone AFSK on USB G2E05 G8A09
Typical exchanges are limited to call signs, grid locators, and signal reports
G2E11
Must use computer timing accurate to 1 second. G2E15
Joe Taylor WSJT-X
JT65, JT9, FT8 use USB

## Slide 9: Transmitting data
Increase data rate increase bandwidth G8B10
Maximum Symbol Rate (Baud) per Band
- 12 m 300 bauds
10 m 1200 bauds
6 and 2 m 19,600 bauds
1.25 and .70 m 56,000 bauds
G1C11
G1C10
G1C09
G1C08
Notes: Write on Frequency chart.

## Slide 10: Videos
https://www.youtube.com/watch?v=gZx8IcHrLwo
https://www.youtube.com/watch?v=ymo91kP1Fpo
PSK 31
RTTY