## Slide 1: Week 4
Radio Signals and Equipment
Sections:
G4A
G4B
G4C
G4E
G4D
G7B
G7C
G8A
G8B
ARRL
Chapter 5
Gordon West
Your HF Transmitter
Your Receiver
Oscillators and Components

## Slide 2: Modulation Modes
AM
FM
PM

## Slide 3: Frequency Shift Keying
FSK. Frequency shift Keying. G8A01
Can be identified as Mark and Space G8C11
AFSK Audio Frequency shift keying
Usually LSB for RTTY. G2E01
If RF is being picked up by an audio cable carrying AFSK data signals between a computer and a transceiver. G4A15
A. The VOX circuit does not un-key the transmitter
B. The transmitter signal is distorted
C. Frequent connection timeouts
AOTA
G8A01 (B)
How is an FSK signal generated?
A. By keying an FM transmitter with a sub-audible tone
B. By changing an oscillator’s frequency directly with a digital control signal
C. By using a transceiver’s computer data interface protocol to change frequencies
D. By reconfiguring the CW keying input to act as a tone generator

## Slide 4: Amplitude Modulation AM
G8A05 Varies the instantaneous power level of the RF signal
Modulation envelope of an AM signal?
The waveform created by connecting the peak values of the modulated signal
G8A11
G8A05 (D)
What type of modulation varies the instantaneous power level of the RF signal?
A. Frequency shift keying
B. Phase modulation
C. Frequency modulation
D. Amplitude modulation

## Slide 5: Single Side Band SSB
SSB is the narrowest phone emissions bandwidth. G8A07
Most commonly used voice mode on the HF amateur bands. G2A05
Advantage; Less bandwidth used and greater power efficiency
G2A06
Only one sideband is transmitted; the other sideband and carrier are suppressed G2A07

## Slide 6: Angle Modulated Modes: FM, PM
G8A02 Phase Modulation (PM) is the process that changes the phase angle of an RF wave to convey information.
G8A03 Frequency Modulation ( FM)
is the process which changes the instantaneous frequency of an RF wave?
PM is produced by a reactance modulator connected to a transmitter RF amplifier stage G8A04
G8A03 (D)
What is the name of the process that changes the instantaneous frequency of an RF wave to convey information?
A. Frequency convolution
B. Frequency transformation
C. Frequency conversion
D. Frequency modulation

## Slide 7
Demodulator
Detector
Modulator
Filters
Multiplier
Our Basic Building Blocks
Oscillator
Produces a steady signal at a single frequency
G7B07
Increases frequency by a whole number multiple
G8B04
Combines two signals
Heterodyning G8B03, G8B01, G8B11
Removes information from modulated RF
Removes or blocks unwanted signals
G7C01
Puts information on the RF signal
G8A04, G7C02
Product
Detector
Detects CW & SSB
G7C04
Frequency
Discriminator
Removes information from FM signals
G7C08
Converts modulated RF
directly into data or voice
G7C07
Mixer
Amplifier
Increases the amplitude of a signal

## Slide 8: Super Heterodyne Receiver
Mixer
Local Oscillator
Filter
RF
Amp
IF
Amp
Detector
AF
Amp
“Front End”
IF Amplifier
Detector
Discriminator
Audio
BFO
Filter
Tunes Input frequency
Converts, (mixes) to produce IF
Filters out all but IF
Amplifies a fixed IF
Signal processing
ADC – DAC
Bandpass filtering
Removes information from IF
FM, SSB, AM
Audio amplify and processing
BFO inserts signal in IF at product detector for SSB

## Slide 9: Oscillator
Oscillator
Amplifier
Output
Feedback circuit
with a filter
G7B07
LC Oscillator, The LC value of the tank circuit determines the frequency. G7B09

## Slide 10: Mixer
Mixer
Mixer
Oscillator
f1
f2
f1 + f2
Mixing also known as heterodyning G8B03
LO
G8B01 Local oscillator
is varied or tuned to convert signals of different frequencies to an intermediate frequency (IF)?
The sum and the difference of the LO and input RF freq. will be found at the output of the mixer. G8B11
9 MHz
11 MHz
10 MHz
1 MHz
1 MHz
10 MHz

## Slide 11: Multiplier
Multiplier
Input f1
Output f2
N = 2, 3, 4, ….
G8B04
A multiplier in a VHF FM transmitter generates a harmonic of a lower frequency signal to reach the desired operating frequency?

## Slide 12: Modulators
Modulator
Carrier input
f1
Modulating input
f2
Output, f1
modulated by f2
A reactance modulator produces FM or PM signals
G8A04
A balanced modulator produces AM or SSB
G7C02

## Slide 13: Balanced Modulator To produce SSB
Carrier signal F1
Special type of mixer
Speech amplifier
LSB
USB
carrier removed
Advantage of carrier suppression
Transmitter power can be used more effectively
A Filter is used to process signals from the balanced modulator
G7C01
Balanced modulator
G7C02
Filter

## Slide 14: FM Modulators
FM output
Reactance modulator
AF
AMP
Audio
Input

## Slide 15: Phase Modulators
Reactance modulator
AF
AMP
PM output
Fixed Frequency
Audio
Input
Phase modulation is produced by a reactance modulator connected to an RF power amplifier? G8A04
RF
AMP

## Slide 16: Transmitter Structure (AM)
G7C02
Which circuit is used to combine signals from the carrier oscillator and speech amplifier and send the result to the filter in a typical single-sideband phone transmitter?
G7C01
Which of the following is used to process signals from the balanced modulator and send them to the mixer in a single-sideband phone transmitter?
Balanced Modulator
Filter

## Slide 17: Transmitter Structure (FM)
It is less expensive and more practical to generate FM signals at low frequencies
and multiply them to the desired frequencies.
Also the deviation is multiplied with each harmonic
AF
AMP
Audio
Input
Reactance
Modulator
Filter
AMP
Multiplier
Antenna
What is the frequency deviation for a 12.21-MHz reactance-modulated oscillator in a 5-kHz deviation, 146.52-MHz FM-phone transmitter?
A. 101.75 Hz
B. 416.7 Hz
C. 5 kHz
D. 60 kHz
(B)
146.52-MHz
5kHz deviation
12.21-MHz
X 12
146.52 MHz
12.21. MHz
=
12
5 kHz
12
= 416.7 Hz
G8B07

## Slide 18: Carson’s Rule
Bandwidth = 2x (peak deviation + highest modulating frequency)
G8B06
What is the total bandwidth of an FM-phone transmission having a 5 kHz
deviation and a 3 kHz modulating frequency?
A. 3 kHz
B. 5 kHz
C. 8 kHz
D. 16 kHz
(D)
FM repeater use only available above 29.5 MHz (upper 10 meter band) G1A15

## Slide 19: Distortion on an SSB signal
Over Modulation
Clipping (flat topping)
Both cause distorted sounding audio.
Both can create spurious signals.
Can be controlled by reducing microphone gain
Speak farther away from the microphone
Caused by driving the amplifier past the point of maximum output. G8A10
Reduce the amplifier drive

## Slide 20: Signal Quality
Over Modulation
ALC, Automatic Level Control
Helps control over modulation
Reduces modulator power output on voice peaks
Adjust ALC to activate on voice peaks.
The ALC is set by the transmit audio or mic gain control. G2A12
If a transceiver’s ALC system is not set properly when transmitting AFSK signals with the radio using single sideband mode. G4A14
It can distorts the signal and can cause spurious emissions

## Slide 22: Speech Processing
Increases average power of the speech signal with out distortion. G4D02
Improves intelligibility of the speech signal. G4D01
The processing is accomplished by compression
Upper voice peaks
Softer voice levels
Voice audio levels
dB
40 dB
30 dB
20 dB
10 dB
Compression 10 db

## Slide 23: Drawbacks of Speech Processing
Improper Adjustment of Compression levels
Distorted Speech
Splatter
Excessive background pickup
G4D03
AOTA

## Slide 24: Over Deviation FM & PM
G8A08
Which of the following is an effect of over-modulation?
A. Insufficient audio
B. Insufficient bandwidth
C. Frequency drift
D. Excessive bandwidth
(D)

## Slide 25: Digital Modes PSK 31
Keep transmit audio low.
Adjust ALC level to not activate ALC meter.
Excessive audio drive

## Slide 26: Amplifiers
Linear amplifier
An amplifier in which the output preserves the input waveform G7B10
Class B
Class A
Class C
Class AB
Most linear
Low Distortion
Low Gain
Least efficient
Always on
Linearity good
Efficiency good
Push Pull design
Each half operates for half of the cycle
Operates midway between A and B
Operates more than 180 o of the cycle
Not as linear as class A
More efficient than class A
Used for SSB operation
Highest efficiency G7B02
Poor linearity
Only suitable for FM or CW G7B11
Efficiency = Output Power / DC Input Power
G7B08
G7B08 (B)
How is the efficiency of an RF power amplifier determined?
A. Divide the DC input power by the DC output power
B. Divide the RF output power by the DC input power
C. Multiply the RF input power by the reciprocal of the RF output power
D. Add the RF input power to the DC output power
~~

## Slide 27: Tuning and Driving an Amplifier

## Slide 28
Peak the load
Maximum power output without exceeding maximum allowable plate current
G4A08
Never exceed maximum drive power G4A07
Neutralize, limit self oscillation
G7B01

## Slide 29
Flash Cards
Public Service
Announcement

## Slide 30: Receiver Structure
“You can’t work ‘em if you can’t hear ‘em.”
G8B09 Match the receive bandwidth to the received signal for better signal to noise ratio

## Slide 31: Super Heterodyne Receiver
Mixer
Local Oscillator
Filter
RF
Amp
IF
Amp
Product
Detector
Beat Frequency
Oscillator BFO
AF
Amp
“Front End”
The mixer processes signals from the RF amp and LO and sends to the IF G7C03
The Product Detector is used to de-modulate SSB and CW. G7C04
Direct digital synthesizer G7C16
Highly stable VFO in a transceiver
Variable frequency with the stability of a crystal oscillator. G7C05

## Slide 32: Super Heterodyne Receiver
Mixer
Local Oscillator
Filter
RF
Amp
IF
Amp
Product
Detector
Beat Frequency
Oscillator BFO
AF
Amp
“Front End”
Limiter +
Discriminator or
Quadrature Detector
The Discriminator is used to de-modulate FM. G7C08

## Slide 33: KISS
G7C07
What is the simplest combination of stages that implement a super-heterodyne receiver?
A. RF amplifier, detector, audio amplifier
B. RF amplifier, mixer, IF discriminator
C. HF oscillator, mixer, detector
D. HF oscillator, pre-scaler, audio amplifier
(C)
HF Oscillator
Mixer
Detector
Audio

## Slide 34: Image Response
455 kHz IF
13.800 MHz
14.255MHz
13.345 MHz
The 13.345 MHz signal is called an Image
Image rejection accomplished by specific filtering in the receivers front end.
G8B02
14.255 – 13.800 = 455
13.800 – 13.345 = 455
G8B02 (B)
If a receiver mixes a 13.800 MHz VFO with a 14.255 MHz received signal to produce a 455 kHz intermediate frequency (IF) signal, what type of interference will a 13.345 MHz signal produce in the receiver?
A. Quadrature noise
B. Image response
C. Mixer interference
D. Intermediate interference
~~

## Slide 35: Filters
G7C13. The filter’s maximum ability to reject signals outside its passband.
Ultimate rejection
G7C14 The bandwidth of a band-pass filter is measured between upper and lower half power point
G7C15 Insertion loss is a filter’s attenuation inside its passband
G7C12 Cutoff frequency is when the filter’s output power is less than half the input power
G7C06 impedance of a low-pass filter as compared to the impedance of the transmission line into which it is inserted should be about the same.
G7C13 (D)
What term specifies a filter’s maximum ability to reject signals outside its passband?
A. Notch depth
B. Rolloff
C. Insertion loss
D. Ultimate rejection
The half power point is point measured at 3 db down.
G7C12 (C)
What is the frequency above which a low-pass filter’s output power is less than half the input power?
A. Notch frequency
B. Neper frequency
C. Cutoff frequency
D. Rolloff frequency

## Slide 36: Removing received interference
Notch Filter
Used to reduce interference from carriers in the receiver passband G4A01
IF shift filter
Used to avoid interference from stations very close to the receive frequency G4A11
Interfering signal
Passband

## Slide 37: Noise Reduction
Noise blanker: Reduces receiver gain during a noise pulse. G4A16
Too much noise reduction can cause signal distortion. G4A17

## Slide 38: Removing received interference
Reverse Sideband for CW
It may be possible to reduce or eliminate interference from other signals G4A02
Interfering signal

## Slide 39: Digital Signal Processing DSP
DSP
ADC
DAC
AF
From mixer or
IF amp
Notch filtering
Can provide automatic notching
Signal filtering,
Wide range
Many choices
Noise reduction
A wide range of filter bandwidths and shapes can be created G4C12

## Slide 40: Receiver Gain.
Manual gain control or
Automatic Gain Control (AGC)
S-Meter
S-Meter reads received signal strength 0 – 9 and + dB over
1 S-unit usually = to 6dB G4D04 G4D07
Receiver S-Meter is found on most receivers G4D06
20 dB over = 100 times stronger
than S9 G4D05
A received signal from S8 to S9 is an increase of approx. 4 times. G4D07

## Slide 41: Software-Defined radios SDR
A radio in which most major signal processing functions are performed by software G7C11
Quadrature Modulation
or
I Q Modulation
+90º
phase shift
network
LO
+
Q
I
RF out
Combiner
All types of modulation G7C10
90º difference between I and Q
G7C10 (B)
What is an advantage of using I and Q signals in software-defined radios (SDRs)?
A. The need for high resolution analog-to-digital converters is eliminated
B. All types of modulation can be created with appropriate processing.
C. Minimum detectible signal level is reduced
D. Converting the signal from digital to analog creates mixing products
~~

## Slide 42: Front End Overload.
Front end of a receiver can be overloaded by a strong signal.
This overloading can cause:
Signal distortion in all signals
Non-linearity of received signal
To correct the problem the operator should use:
The built in attenuator circuit G4A13
RF Gain control
Front end filtering to eliminate the strong signal
G4A13 (A)
What is one reason to use the attenuator function that is present on many HF transceivers?
A. To reduce signal overload due to strong incoming signals
B. To reduce the transmitter power when driving a linear amplifier
C. To reduce power consumption when operating from batteries
D. To slow down received CW signals for better copy

## Slide 43: Station Installation HF
Mobile Installation:
Use heavy gauge wire connected with a fuse directly to the battery. G4E03
On most vehicles, the aux power socket or light socket is not designed for high current. G4E04
The mobile antenna system is the limiting factor for effectiveness in the 75 meter phone band. G4E05
Mobile interference: G4E07
A. The battery charging system
B. The fuel delivery system
C. The vehicle control computer
AOTA

## Slide 44: Station Installation HF
Station Grounding.
To RF, long ground wires act like antennas.
Ground all equipment to a common bus.
Keep all connections, straps, and wires short
Connect ground bus to a ground rod.
Ground wires a a quarter wave multiple to the
operating frequency offer a high impedance to RF.
Can cause high RF voltages on equipment housing. G4C06

## Slide 45: Station Installation HF
Station Grounding.
Ground Loops
Caused by a continues grounding system acting like an inductor and picking up stray magnetic energy.
Results in a hum or buzz on the station’s signal. G4C10
Connect all grounding wires to a single point. G4C09

## Slide 46: For Next Week
Study flash cards www.hamexam.org
73
Tom and Jack
Lesson 1
G1A
G1C
G2A
G2B
G4A part
G4D part
G8A
Lesson 9
G4E
G9A
G9B
G9C
G9D
Lesson 7
G4A
G4B
G4C
G4D
G7B
G7C
G8A
G8B
Lesson 4
G5A
G5B
G6A
Lesson 11
G0A
G0B
Radio
Fundamentals
ARRL Ch. 1, 2, 3, 6
Antennas
ARRL Ch. 7
Electricity
ARRL Ch. 4
Safety
Ch. 9
Lesson 3
G5B
G5C
Resistors
Capacitors
AC Power
The Reactive
components
Lesson 5
G4B
G4E
G6A
G6B
G7A
G7B
Semi-
conductors
Propagation
ARRL Ch. 8
Lesson 8
G3A
G3B
G3C
Digital
ARRL Ch. 6
Lesson 10
G2C
G2E
G8A
G8B
G8C
Lesson 2
G1B part
G2B
G2C
G1D
G1E part
G8C part
General
Intro
Rules & Regs
Equipment
ARRL Ch. 5
Lesson 6
G4E
G9A
G9B
G9C
G9D
Radio signals
And equipment
Equipment
Cont.
ARRL Ch. 5
Filters, DSP
Station Installation
Antennas
Feedlines
Propagation