What mode am I in?

If you are in memory mode. The FT-60 will display "MEMORY " when first turned on. Then it will go to a display that shows frequency, a channel number, along additional info depending on settings.

If you are in frequency or V mode.  The display will display a frequency along with additional info depending on settings, no channel number.

The V/M button on the lower left will toggle between the two modes.

To manually enter a frequency.

- You must be in frequency mode.

2. Enter the six digits of the frequency you want.

In the band plan for 2 meters and 70 cm. frequencies are designated for simplex and repeater use.  The radio knows the band plan.  If the frequency you chose is a repeater frequency, a + or - will be displayed. If it is a simplex frequency, there will be no + or -.  The radio also knows the appropriate offset direction.

To enter the proper tone for repeater use.

At any time you enter an error, just press your transmit to return to previous

1. Enter a repeater frequency in frequency mode.

2. Press the function key (F), lower right

3. Press #1 (SQ TYP)

4. Rotate tuning knob, top right, until you get a display of  T TONE.

5. Again press F

6. Press F

7. Press #2 (CODE) rotate tuning knob to the proper tone (PL frequency)

Press F

Now when you transmit, the frequency will indicate the repeater input frequency + or - 600 kHz.  When you let up on the transmit, the display will indicate the frequency you entered, which is your receive frequency and repeater transmit frequency.

Remember we are still in the frequency mode.

If you want to put this frequency in memory.

1. Press and hold F until you hear the double beep.

2. The radio will automatically go to an empty channel location.

Or rotate tuning knob to a channel of your choice

3. Press F again and the frequency is now in a memory position.

In memory mode you can now recall that location which now holds your desired frequency and parameters.

For a simplex frequency, transmit and receive are on the same frequency,

1. Go to frequency mode

2. Enter the desired frequency (there will not be a + or - in the display) of a simplex frequency in the band plan.

If a T displays, not to worry.

You are now ready to transmit in simplex.

You choice if you want to assign a memory location for the frequency.

Example

To Enter 146.550 simplex.

1. Select frequency mode.     V/M

2. Enter 146550

Transmit on simplex 146.550

There are many more functions that the FT-60 will perform, but this will get you on the air.

Caution.  In the upper right hand corner of the display there is a symbol when WIRES is activated.  (Crossed ellipse). This is controlled by the # 0 key.  Leave this function off.  If you hear a beep every time you transmit it is activated.  Just press 0 to remove.

To permanently disable, go to http://www.w4cll.com/PDF/WIRES/YaesuWIRES.pdf

# Text boxes

The Yaesu FT-60 is a widely popular hand held radio.  Often times we just grab the radio and use it for our check-ins, not giving much thought to the programming procedures.  There is Nifty Quick-Reference guide available from niftyaccessories.com.  I keep one in my go bag for reference.  I thought I would give a simple programming cheat sheet to help all to jog the brain to the programming.

The FT-60 has two operating modes.  Memory (M) and Frequency (V).  The lower left button switches the modes. F/V